## Slide 1: ABS 38W Female Connector Assy

## Slide 2: ABS 38W Female connector
38 Way ABS Connection
Technology Advantage
  Standard interface with header
  High density circuits application
  High performance terminal system
  Simplified MFG and assembly process
  Alternative wire harness outlet direction
  Low operation force with Level lock
  Cost savings
Availability
  Available for VW group , Ford , HYUNDAI
Application
  Sealed type;
    IP 67
  Temperature range:
    -40℃~105℃
  Current range:
    Terminal 1.5 F, 19A Max
    Terminal 2.8 F, 30A Max
    Terminal 4.8 F, 40A Max
  Cable range:
    Terminal 1.5 F, 0.35—1.5 mm2
    Terminal 2.8 F, 1.0—2.5 mm2
    Terminal 4.8 F, 2.5—4.0 mm2
  Packaging size:
        85.6 X 36.2 X 55.7mm

## Slide 3: ABS 38W Female connector
Description | PIC | Series | PN | M. Site | Drawing NO.
Female connector housing |  | Lever left, Wire right | 13579681(Code 0) | China | 15498537_CUS01_S01.pdf
 |  |  | 13863402(Code 1) | China | 13653053_CUS01_S01.pdf
 |  |  | 13670757(Code 2) | China | 15498537_CUS01_S01.pdf
 |  |  | 15498536(Code 3) | China | 15498537_CUS01_S01.pdf
 |  | Lever right, Wire left | 13653052(code 0) | China | 13653053_CUS01_S01.pdf
 |  |  | 13598001(code 1) | China | 13653053_CUS01_S01.pdf
 |  |  | 13598002(code 2) | China | 13653053_CUS01_S01.pdf
Cover |  | Horizontal(with no CPA) | 13598000 | China | 13598000_CUS01_S01.tiff
 |  | Horizontal(with CPA) | 13653051 | China | 13653051_CUS01_S01.tiff
 |  | Vertical(no CPA) | 15498543 | EU | 15498544_CUS54_S01.tiff

## Slide 4: ABS 38W Female connector
Title | Terminal PN | M. Site | Plating | Drawing NO. | Wire Size Range(mm2) | Cable Seal PN | M. Site | Drawing NO. | Cavity Plug PN | M. Site | Drawing NO.
Female Terminal CTS 150 | 15432208 | China | Sn | 15432214_CUS02_S01.tiff | 0.35mm2 | 15327913(1.2mm-1.6mm) | China | 15446589_CUS53_S01.tiff | 12198198 | EU | 13661690_CUS51_S01.pdf
 | 15432210 | China | Sn |  | 0.5-0.75mm2 | 15327918(1.2-2.0mm) | China |  |  |  | 
 | 15432212 | China | Sn |  | 1-1.5mm2 | 15339412( 1.9-2.1mm ) | EU |  |  |  | 
Female Terminal CTS 280 | 15446673 | EU | Sn | 15446676_CUS02_S01.pdf | 0.35mm2 | 15327860(1.2-2.0mm) | Korea |  | 15337197 | EU | 13688485_CUS51_S01.pdf
 | 15446674 | EU | Sn |  | 0.5-1mm2 | 15327863(2.0-2.7mm) | EU |  |  |  | 
 | 15446675 | EU | Sn |  | 1.5-2.5mm2 | 15327859(2.7-3.0mm) | EU |  |  |  | 
Female Terminal CTS 480 | 13976114 | EU | Sn | 13976112_CUS01_S01.pdf | 0.35mm2 | 15363779(1.2-2.0mm) | EU |  | 12066082 | NA | 12124630_CUS01_S01.pdf
 | 13976115 | EU | Sn |  | 0.5-1.0mm2 |  |  |  |  |  | 
 | 13976116 | EU | Sn |  | 1.5-2.5mm2 | 15363604(2.0-2.7mm) | EU |  |  |  | 
 | 13976117 | EU | Sn |  | 2.5-4mm2 | 15327864(2.8-3.8mm) | EU |  |  |  | 
 | 13976118 | EU | Sn |  | 4-6mm2 | 15363605(4.0-4.5mm) | EU |  |  |  |